## Slide 1
AI-Powered Fault Detection in Power Distribution Lines
Intelligent real-time monitoring system using Arduino and machine learning to detect electrical faults before they cause damage

## Slide 2
Project Objective
Real-Time Monitoring
Continuously monitor power distribution lines for electrical anomalies
Fault Detection
Identify short circuits, overloads, voltage sags and swells using AI
Intelligent Alerts
Provide predictive warnings through smart dashboard system

## Slide 3
Why Is It Useful?
Critical Safety
Power grid faults cause dangerous outages and equipment damage
Traditional Limitations
Existing relays and circuit breakers are slow and reactive
AI Advantage
Predictive detection based on voltage and current patterns
IoT Integration
Remote monitoring with real-time dashboard alerts

## Slide 4
System Architecture Flow
01
Data Acquisition
Arduino Uno with current (ACS712) and voltage (ZMPT101B) sensors sampling at 1 KHz frequency
02
Data Preprocessing
Python script processes serial data, filters noise, calculates RMS values and power metrics
03
Feature Extraction
Extract RMS voltage/current, power factor, harmonic content using FFT analysis
04
AI Model Training
Random Forest Classifier trained on labeled normal vs fault data patterns
05
Real-Time Detection
Continuous monitoring with instant fault classification and alert generation
06
User Interface
Streamlit dashboard displaying live plots, status, and fault type identification

## Slide 5
Arduino vs AI Roles
Arduino Uno
Role: Data acquisition and preprocessing
Tasks: High-frequency voltage/current sampling, serial transmission
Strength: Hardware-level sensing, fast sampling, easy prototyping
Limitation: Limited compute power for AI processing
AI Model (Python)
Role: Intelligent fault classification
Tasks: Pattern analysis, trained model predictions, alert generation
Strength: Processes complex non-linear patterns and harmonics
Requirement: Needs training data for accurate pattern recognition

## Slide 6
System Block Diagram
Power Line Sensors
Current sensor (ACS712) + Voltage sensor (ZMPT101B) measure electrical parameters
Arduino Uno Processing
Analog data sampling and serial/Wi-Fi transmission to PC
Python ML Pipeline
Feature extraction (RMS, FFT, Power Factor) and AI model processing
Fault Classification
Random Forest model outputs Normal/Fault status with type identification
Alert Dashboard
Real-time display of system status and fault notifications

## Slide 7
Project Advantages & Deliverables
Why This Approach Is Better
AI detects complex patterns beyond simple thresholds
Adaptive to different line types and environmental changes
Cost-effective prototyping with Arduino and Python
Final Deliverables
Working hardware prototype
Labeled training dataset
Trained AI model (.pkl file)
Real-time detection demo
Comprehensive project report